## Slide 1: IEEE HACKATHON
Team Name: ATOM ROBOTICS
Theme: Surveillance, Mapping for disaster management
Target: Aiming to aide rescue operations in GPS denied areas with aerial robots to navigate autonomously irrespective the terrain or environment (Indoor-Outdoor). Majorly used when finding the trapped as a result of debris, forest fire operations, examining damaged infrastructures, warehouse monitoring, etc.
Team Members: Jerrin Bright; Suryaprakash R

## Slide 2: OBJECTIVE
Accurate navigation in GPS-restricted environments using the State-of-the-Art visual SLAM technique.
Removal of dynamics features thus making suitable for real-time test scenarios as most of the drone enthusiasts consider working in static scenarios.
Dynamic Obstacle Avoidance using Panoptic and Optical Flow.
Optimization of drone frame using Generative Designing technique.
PROBLEMS
GPS
FEATURES
FRAME

## Slide 3: DESIGNING OF THE FRAME
Component | Pieces | Net Weight (gm) | Cost (INR)
RS2205S Motor (2700kv) | 4 | 115.2 | 3000
Pixhawk FC | 1 | 73 | 5000
M8N GPS | 1 | 32 | 2000
5” Propeller | 4 | 16 | 300
BL Heli ESC (40A) | 4 | 56 | 4000
PC Hub PDB | 1 | 8.5 | 700
Camera | 2 | 900 | 4000
Telemetry | 1 | 15 | 2000
LiPo Battery (5200mah) | 1 | 200 | 5000
Onboard Custom CPU | 1 | 400 | 20,000
TOTAL | 18 | 1815.7 | 50,000
LOAD CONDITIONS
Iterative design exploration process
Uses AI to generate multiple design
Mass reduction and structural optimization
GENERATIVE DESIGNING

## Slide 4
SIMULATION RESULTS
VON-MISES STRESS STATIC STRAIN
DISPLACEMENT MODULAR FREQUENCY
Mass of Frame (Lf)= 400gms
External Load (Le)= 1800gms
M = Lf + Le = 2200gms = 2.2kg
F = M x g = 22N
Wheelbase = 450mm
This implies that each and every motor should have a thrust of 22N/4 = 5.5N.
AFTER GENERATIVE DESIGNING
BEFORE GENERATIVE DESIGNING

## Slide 5: Generative Designing (GD) Technique
All the designs generated are within the safety limit
Mass is comparatively less for generatively designed frames when compared to traditionally designed drone frame
Factor of safety of our frame is almost 4 times of DJI F450 Drone frame
Maximum displacement of our frame is just about 0.6 mm under the loading conditions which is 10 times when compared to DJI Drone frame
Von misses stress is 11.4 times less for our frame in comparison to DJI F450 Frame
Our frame can withstand cyclic load and can survive from failure for a longer period of time
Link for our paper: https://iopscience.iop.org/article/10.1088/1757-899X/1012/1/012019

## Slide 6
Computing pose and the map of environment simultaneously
Localization – estimating the robot’s location
Mapping – building a map and
SLAM – building a map and localizing the robot simultaneously
 | CAMERA | LIDAR | RADAR
Computation | 3 | 1 | 2
Weight | 1 | 3 | 2
Cost | 1 | 3 | 2
Weather Dependency | 2 | 3 | 1
Heat | 1 | 3 | 2
Range | 3 | 2 | 1
WHY VISUAL SLAM?
WHAT IS SLAM?
A B

## Slide 7
ARCHITECTURE OF VINS

## Slide 8
IMPLEMENTATION OF VINS

## Slide 9
DYNAMIC FEATURE REMOVAL

## Slide 10
DYNAMIC OBSTACLE AVOIDANCE
Using,
Optical Flow
Panoptic Segmentation

## Slide 11
Navigation in GPS-denied environments
Dynamic features Removal
Optimized drone frame
Dynamic Obstacle Avoidance.
Used for:
  finding the trapped as a result of debris,
  forest fire operations,
  examining damaged infrastructures,
  warehouse monitoring, etc.
Concluding Note

## Slide 12: REFERENCES
T. Qin, P. Li and S. Shen, "VINS-Mono: A Robust and Versatile Monocular Visual-Inertial State Estimator," in IEEE Transactions on Robotics, vol. 34, no. 4, pp. 1004-1020, Aug. 2018, doi: 10.1109/TRO.2018.2853729.
S. Han and Z. Xi, "Dynamic Scene Semantics SLAM Based on Semantic Segmentation," in IEEE Access, vol. 8, pp. 43563-43570, 2020, doi: 10.1109/ACCESS.2020.2977684.
Hell, Peter & Varga, Peter. (2019). Drone Systems for Factory Security and Surveillance. Interdisciplinary Description of Complex Systems. 17. 458-467. 10.7906/indecs.17.3.4.
Jerrin Bright et al 2021 ”Optimization of quadcopter frame using generative design and comparison with DJI F450 drone frame” IOP Conf. Ser.: Mater. Sci. Eng. 1012 012019

## Slide 13: Thank You!
Atom Robotics